# Division of two 8-bit numbers

## Algorithm
1. Start the program by loading HL register pair with address of memory location.
2. Move the data to a B register.
3. Get the second data and load into Accumulator.
4. Compare the two numbers to check for carry.
5. Subtract the two numbers.
6. Increment the value of carry .
7. Check whether repeated subtraction is over and store the value of product and carry in memory location.
8. Terminate the program.

## Program

        LXI H, 5000
        MOV B, M ;Get the dividend in B - reg.
        MVI C, 00 ;Clear C - reg for quotient
        INX H ;Increment HL pair of registers
        MOV A, M ;Get the divisor in A - reg
  NEXT: CMP B ;Compare A - reg with register B.
        JC LOOP ;Jump on carry to LOOP
        SUB B ;Subtract A - reg from B - reg.
        INR C ;Increment content of register C.
        JMP NEXT ;Jump to NEXT
   LOOP: STA 5002 ;Store the remainder in Memory
        MOV A, C ;Move Content of C - Reg to A - Reg
        STA 5003 ;Store the quotient in memory
        HLT ;Terminate the program.
Result:
Input:
Data 1: FFH in memory location 5000
Data 2: FFH in memory location 5001

Output:
Data 1: 01H in memory location 5002 as Remainder
Data 2: FEH in memory location 5003 as Quotient